## Slide 1: Take home test #3 Anthony Ramos CSC342/43 spring 2021

## Slide 2: Objective
Implement a program to compute dot product using Pointer Arithmetic (discussed here)
Utilize QueryPerformanceCounter() to measure execution times (Visual Studio Only)
Optimize compiler generated assembly code using vector instructions
Simulate in MS Visual Studio and Linux environments
Repeat using array indexing instead (See report)

## Slide 3: My CPU Info
My CPU’s instruction capabilities

## Slide 4: My CPU Info
(cpubenchmark.net)

## Slide 5: Dot Product Program
See Report

## Slide 6: QueryPerformancecounter()

## Slide 7: Optimization Settings (Auto parallelization/Vectorization)
Enable Auto
Vectorization
Enable Auto
Parallelization

## Slide 8: Test File
Link functions
Dot Product (Array Indexing)
Dot Product (Pointer Arithmetic)
Dot Product (SSE3 Vector Instructions)
Fill array values (we are not concerned with the result)
Note: We must change the
datatypes of arr1, arr2, result, and i from int to float if we want to use test DotProduct_Vector()

## Slide 9: Dot Product (Vector Instructions)

## Slide 10: results(MS Visual studio)
Chart: Execution Times (Pointer)
| 16 | 32 | 64 | 128 | 256 | 512 | 1024 | 2048 | 4096 | 8192 | 16384 | 32768 | 65536 | 131072 | 262144 | 524288 | 1048576
No Optimization | 3.4e-07 | 4e-07 | 5.2e-07 | 7.2e-07 | 9.6e-07 | 2.16e-06 | 3.6625e-06 | 6.1375e-06 | 1.3833e-05 | 2.9011e-05 | 4.735e-05 | 9.5411e-05 | 0.000192 | 0.0004518 | 0.00081098 | 0.0016507 | 0.0033125
Compiler Optimized | 3e-07 | 4.2e-07 | 4.2e-07 | 6.6e-07 | 9.6e-07 | 1.53e-06 | 2.825e-06 | 5.825e-06 | 9.625e-06 | 2.1737e-05 | 3.8475e-05 | 8.0988e-05 | 0.00018367 | 0.0003659 | 0.00067712 | 0.0011808 | 0.0021571
SSE3 Vector Instructions | 4.4286e-07 | 5.1429e-07 | 5.4286e-07 | 6e-07 | 6.7143e-07 | 7e-07 | 1.0667e-06 | 1.2556e-06 | 2.2e-06 | 4.8e-06 | 8.2778e-06 | 1.92e-05 | 3.9889e-05 | 0.00010551 | 0.00018434 | 0.00042722 | 0.00083767

## Slide 11: Optimization in a Linux environment
Optimization Flag | Optimization Level | Execution Time | Notes
-O0 | 0 (Default) | + | No Optimization
-O1 | 1 | - | Basic Optimization
-O2 | 2 | -- | Recommend Level
-O3 | 3 (Highest) | --- | Optimization Not Guaranteed
GCC optimization - Gentoo Wiki
Optimize Options (Using the GNU Compiler Collection (GCC))
Attempts to
vectorize loops

## Slide 12: Optimization in a Linux environment
clock_gettime()
Call both functions via extern
Perform 1000 runs for each
program

## Slide 13: Optimization in a Linux environment
Optimization Flags
No Optimization
Level 1 Optimization
Level 2 Optimization
Level 3 Optimization

## Slide 14: Results (Linux)
Chart: Execution Time At Various Optimization Levels (Pointer)
| 16 | 32 | 64 | 128 | 256 | 512 | 1024 | 2048 | 4096 | 8192 | 16384 | 32768 | 65536 | 131072 | 262144 | 524288 | 1048576
Optimization Level 0 | 6.55e-07 | 7.55e-07 | 8.22e-07 | 1.098e-06 | 1.817e-06 | 2.563e-06 | 4.202e-06 | 2.5473e-05 | 3.4611e-05 | 6.4762e-05 | 0.00012193 | 0.00023343 | 0.00048188 | 0.00088907 | 0.0018937 | 0.0037478 | 0.0076774
Optimization Level 1 | 5.43e-07 | 6.07e-07 | 8.17e-07 | 1.005e-06 | 1.645e-06 | 2.274e-06 | 3.579e-06 | 4.211e-06 | 2.5928e-05 | 3.2788e-05 | 6.3483e-05 | 0.00016343 | 0.00028261 | 0.00042249 | 0.00090548 | 0.0016764 | 0.0038049
Optimization Level 2 | 5.14e-07 | 5.63e-07 | 6.4e-07 | 7.18e-07 | 1.422e-06 | 1.881e-06 | 2.206e-06 | 3.988e-06 | 1.6503e-05 | 2.5733e-05 | 4.9134e-05 | 0.00012625 | 0.00022527 | 0.00038853 | 0.00088314 | 0.0013682 | 0.0033441
Optimization Level 3 | 5.12e-07 | 5.34e-07 | 7.31e-07 | 5.69e-07 | 1.011e-06 | 1.912e-06 | 2.23e-07 | 3.231e-06 | 1.5178e-05 | 3.2438e-05 | 5.027e-05 | 0.00013249 | 0.00022556 | 0.00039254 | 0.00087827 | 0.0013274 | 0.0032563
See report for results via array indexing

## Slide 15
Thank You!